## Slide 1
{ }
Wait Less | Sapienza IoT - Final Delivery
Software | general structure
Software is a pipeline from sensing to evidence.
The code is not only a simulator: firmware, shared logic, logging tools, and replay all use the same data story.
Sensors
4 ultrasonic
far + near
->
Firmware
Node A + Node B
ESP32 LoRa
->
Shared logic
sensing, queue,
controller, packets
->
Logger
serial B STATUS
saved CSV
->
Evaluation
TP/TN/FP/FN
stale + energy
->
Simulator
CSV replay
digital twin
Repository structure used in the software slides
firmware/node_a/main.cpp // Side A sensing + LoRa TX
firmware/node_b/main.cpp // Side B sensing + control
lib/traffic_control/ // shared logic used by both nodes
tools/road_data_logger.py // live serial -> CSV evidence
tools/final_evidence_report.py // metrics and report
simulation/visual_simulator.py // CSV replay / digital twin
What this proves to the professor
- Real sensor readings are converted into queue states.
- Node A and Node B communicate through LoRa packets.
- Node B makes the final light decision locally.
- The same live log becomes CSV, metrics, graphs, and simulator replay.
- Improvements are visible in code: filtering, stale handling, emergency, energy logging.
Speaker message: each later slide zooms into one layer of this pipeline, then shows how we improved it after testing.

## Slide 2
A/B
Wait Less | Sapienza IoT - Final Delivery
Software | node firmware
Node A senses; Node B decides and controls.
The two ESP32 programs have different roles, but they share the same telemetry and sensing model.
Node A responsibilities
- read A_far and A_near
- filter + debounce occupancy
- estimate Side A queue
- encode LoRa telemetry
- print human-readable status
Node B responsibilities
- read B_far and B_near
- receive Node A telemetry
- detect stale LoRa
- run adaptive controller
- drive all six LEDs and log CSV line
Node A: sensor state becomes LoRa payload
SideTelemetry telemetry =
laneEstimator.update(SideId::A,
farOccupied, nearOccupied, nowMs);
telemetry.farDistanceCm = farDistance;
telemetry.nearDistanceCm = nearDistance;
const String payload = encodeTelemetry(telemetry);
sendTelemetryOverLoRa(payload);
Node B: combine A + B, then apply lights
if (loRaTryReceive(packet, Serial)) {
parseTelemetryLine(packet.payload, received);
lastRemoteRxMs = nowMs;
}
SideTelemetry remote = effectiveRemoteTelemetry(nowMs);
TrafficDecision decision =
controller.update(remote, localTelemetry, nowMs);
applyLights(decision.lights);
4
physical ultrasonic readings
1
LoRa direction: A to B
6
LED outputs on Node B
50 cm
live demo threshold
Live demo line proves all roles are active
B STATUS | A_queue=... | B_queue=...
| A_far=...cm/OCC | B_far=...cm/FREE
| source=LORA_RADIO | stale=OFF
| backup=OFF | green=A | lights=A:GREEN B:RED

## Slide 3
lib
Wait Less | Sapienza IoT - Final Delivery
Software | shared code
Shared code keeps the two nodes consistent.
The project avoids two separate implementations by putting sensing, packet, queue, and controller logic in reusable modules.
HardwareMap.h
pin source of truth
A/B sensors, LEDs, button
SensorSupport.cpp
HC-SR04 distance
median3 + debounce2
TrafficSensing.cpp
incoming/passed counters
queue estimate
NodeMessaging.cpp
LoRa CSV payload
backward-compatible decode
AdaptiveController.cpp
demand score
min green + yellow
Ina219Support.cpp
optional current/power
INA219_NA if absent
Reliability layer after real-road testing
- Median filtering rejects one-sample ultrasonic spikes.
- Debounce requires repeated agreement before occupancy changes.
- Sensor health shows WARN/FAIL instead of hiding bad wiring or angle issues.
SensorSupport.cpp: final occupancy is filtered, thresholded, then debounced
reading.distanceCm = readMedianUltrasonicDistanceCm(trigPin, echoPin,
medianSampleCount, timeoutUs);
reading.rawOccupied = isDistanceOccupied(reading.distanceCm, thresholdCm);
reading.stableOccupied = debouncer.update(reading.rawOccupied, debounceSamples);
farHealth.update(farDistance); // status: OK / WARN / FAIL
Speaker message: this slide shows that the software is engineered in layers, so every improvement is implemented once and reused by both boards.

## Slide 4
eq
Wait Less | Sapienza IoT - Final Delivery
Software | adaptive algorithm
The controller scores demand and switches safely.
The algorithm is intentionally explainable: queue pressure is weighted, but timing and emergency rules prevent unstable behavior.
Demand equation
demand = 3 x queue + 2 x farOcc + 4 x nearOcc
Queue length matters most; the near sensor has extra weight because it means a vehicle is at the stop line.
TrafficTypes.h: exact demandScore() used by the firmware
const uint32_t queueWeight = telemetry.estimatedQueue * 3U;
const uint32_t incomingWeight = telemetry.farOccupied ? 2U : 0U;
const uint32_t stopLineWeight = telemetry.nearOccupied ? 4U : 0U;
return queueWeight + incomingWeight + stopLineWeight;
AdaptiveController.cpp: switching is allowed only after safe timing
const bool canSwitch = phaseElapsedMs >= config_.minGreenMs;
const bool currentEmpty = !hasDemand(current);
const bool otherBusy = hasDemand(other);
const bool reachedMaxGreen = phaseElapsedMs >= config_.maxGreenMs;
const bool otherClearlyBusier =
demandScore(other) > (demandScore(current) + config_.advantageMargin);
if (canSwitch && ((currentEmpty && otherBusy) ||
(otherBusy && otherClearlyBusier) || (reachedMaxGreen && otherBusy))) {
beginYellow(other.side, nowMs);
}
Improvements added after problems appeared
- per-sensor threshold commands: set_thresholds 50 50
- median-of-3 ultrasonic filtering
- 2-sample occupancy debounce
- sensor health diagnostics: OK / WARN / FAIL
- emergency button: 1 click = B, 2 clicks = A
- stale Node A backup and recovery logging
Speaker message: the algorithm is not a black box. We can justify every number and explain every improvement as a response to measured behavior.

## Slide 5
LoRa
Wait Less | Sapienza IoT - Final Delivery
Software | communication before
Before improving, sending a packet was not enough.
The first LoRa version proved connectivity, but the professor's point was reliability: what does the packet mean, and is it fresh?
Older payload accepted by the decoder
A,farOccupied,nearOccupied,
incomingCount,passedCount,queue,timestampMs
Example:
A,1,0,4,2,2,12345
NodeMessaging.cpp kept backward compatibility
// Earliest payload without emergency flag or distances
matched = sscanf(payload.c_str(),
"%c,%d,%d,%lu,%lu,%lu,%lu",
&sideToken, &farOccupied, &nearOccupied,
&incomingCount, &passedCount,
&estimatedQueue, &timestampMs);
emergencyRequested = 0;
What was missing
- no real distance values in the packet
- no emergency field in earliest format
- no clear stale/fresh state for Node B
- no way to distinguish no traffic from no node
Why that mattered
- false positives cannot be measured from a packet alone
- old packets can create a phantom queue
- energy saving by silence can look like failure
- logs need enough fields for CSV evaluation
Transition to the final version
The next version adds distances, emergency state, stale detection, backup behavior, and a clean live log. That turns LoRa from a demo packet into useful IoT telemetry.
Speaker message: this is the process slide. We can honestly say the first version was not enough, then show exactly what we changed.

## Slide 6
RX
Wait Less | Sapienza IoT - Final Delivery
Software | communication after
Improved communication carries state and health.
Node B now uses packet freshness, backup mode, and a future heartbeat idea to avoid confusing empty traffic with failure.
Final packet format sent by Node A
side,farOcc,nearOcc,incoming,passed,queue,
emergency,timestampMs,farDistanceCm,nearDistanceCm
Example:
A,1,0,4,2,2,0,12345,42.0,999.0
NodeMessaging.cpp: encodeTelemetry()
return String(sideName(telemetry.side)) + "," +
String(telemetry.farOccupied ? 1 : 0) + "," +
String(telemetry.nearOccupied ? 1 : 0) + "," +
String(telemetry.incomingCount) + "," +
String(telemetry.passedCount) + "," +
String(telemetry.estimatedQueue) + "," +
String(telemetry.emergencyRequested ? 1 : 0) + "," +
String(telemetry.timestampMs) + "," +
String(telemetry.farDistanceCm, 1) + "," +
String(telemetry.nearDistanceCm, 1);
Node B: stale data becomes backup mode, not silent failure
if (lastRemoteRxMs == 0 ||
(nowMs - lastRemoteRxMs) > config::kRemoteTelemetryTimeoutMs) {
setNodeABackupActive(true, "NODE_A_STALE");
remoteTelemetryStale = true;
lastRemoteSource = "LORA_STALE";
return makeNodeABackupTelemetry(nowMs);
}
Future improvement: separate traffic telemetry from heartbeat
if (queue == 0 && farFree && nearFree) {
sendHeartbeatEvery(10000); // alive, no traffic
sendTelemetryOnlyOnChange(); // full packet if state changes
} else {
sendTelemetryEvery(1000); // active traffic mode
}
if (millis() - lastHeartbeatMs > failureTimeoutMs) {
markNodeFailed();
}
Communication improvement
- stale LoRa becomes backup mode
- heartbeat can reduce packets while failure timeout remains active
Important limitation
If Node A sleeps completely, HC-SR04 cannot wake it by itself. True wake-on-car needs a low-power detector such as IR, magnetic, radar, or loop sensor.

## Slide 7
mW
Wait Less | Sapienza IoT - Final Delivery
Software | power and duty cycling
Energy was measured before optimization.
The final demo reports INA219 baseline current, then proposes adaptive duty cycling without hiding node failures.
123.0 mA
Node A measured average
174.8 mA
Node B measured average
297.9 mA
combined baseline
INA219
measured, not guessed
Current firmware: optional INA219 evidence
lastPowerReading = ina219Read();
Serial.print(" | power=");
if (lastPowerReading.ok) {
Serial.print(lastPowerReading.currentMa, 1);
Serial.print("mA/");
Serial.print(lastPowerReading.powerMw, 1);
Serial.println("mW");
} else {
Serial.println("INA219_NA");
}
Proposed improvement: adaptive duty cycle
if (bothQueuesEmpty()) {
telemetryPeriodMs = 10000; // heartbeat / low activity
} else if (isPeakHour() && bothSidesBusy()) {
telemetryPeriodMs = 3000; // saturated traffic: fewer repeated updates
} else {
telemetryPeriodMs = 1000; // normal adaptive control
}
Before improvement
- fixed telemetry interval
- continuous sensing and logging
- Node B radio receive and LED load always active
- baseline measured with INA219
After improvement idea
- full telemetry only when state changes
- heartbeat proves node is alive
- longer failure timeout in idle mode
- optional lower sampling in predictable peak saturation
Sleep mode tradeoff
Periodic ESP sleep saves more energy, but can miss a car during sleep. Reliable wake-on-car needs an external low-power detector, then HC-SR04 confirms distance.
Speaker message: the numbers on this slide are measured baseline values; the duty-cycle logic is a justified future optimization, not claimed as already measured.

## Slide 8
sim
Wait Less | Sapienza IoT - Final Delivery
Software | simulators
The simulator became a real-data replay tool.
We kept random/manual modes for testing, but the important final mode is CSV replay from the road run.
Simulator modes
- CSV replay from road data
- direct queue input
- manual rates
- random traffic
- fixed scenarios
Why CSV replay matters
- uses real sensor demand
- shows queues visually
- compares adaptive vs fixed-time idea
- connects IoT evidence to digital twin
simulation/visual_simulator.py: road CSV becomes replay frames
frames = load_road_frames(path)
self.csv_status_var.set(
"CSV replay loaded: " + csv_status_line(frames, path)
)
// CSV fields used: A/B queues, distances, phase, green side,
// source=LORA_RADIO or LORA_STALE
How to say this honestly
The simulator does not replace field evidence. It replays the measured demand from the road CSV so we can visualize and compare the controller behavior against a fixed-time baseline. That is the digital twin connection.
End of software story: sensors -> firmware -> LoRa -> controller -> log -> CSV -> evaluation -> replay.